## Slide 1
Automated Venipuncture Device
Re-imagining blood collection through robotic precision, computervision and
modular design to eliminate trial-and-error punctures and enhance patient safety.

## Slide 2
The Challenge
Manual Blood Draws: A Problem of
Precision
The core insight: precision and trust are inseparable in clinical care.
Manual venipuncture remains fraught with complications. Multiple failed
attempts cause patient discomfort, anxiety, and increased infection risk. The challenge intensifies for vulnerable populations for infants, elderly patients, pregnant women, and individuals with darker or low-visibility skin tones where vein detection becomes exponentially more difficult. Each puncture attempt strains the trust between patient and clinician.

## Slide 3
Our Vision
Eliminate guesswork with computer vision
Transform trial-and-error into reliable process
Reduce failed attempts and complications
We are building a smart, modular robotic system that automatically identifies
suitable veins, aligns with surgical precision, and performs venipuncture with minimal human intervention for while simultaneously enabling efficient blood sample collection through a modular, adaptable architecture.
Precision
Automation
Safety

## Slide 4
Five-Step System Architecture
04
Controlled Puncture
01
Wearable NIR Belt
02
Real-Time Processing
05
Smooth Extraction
03
Precision Alignment
Infrared imaging captures high-contrast vein visualization across all skin tones.
Piezoelectric actuator penetrates skin to exact depth for 2-3mm precision.
Raspberry Pi analyzes image, maps vein geometry, computes optimal puncture coordinates.
Micro vacuum pumping enables gentle, consistent blood collection.
SO100ARM six-axis robotic arm positions
needle with micrometer accuracy.

## Slide 5
Layered System Intelligence
ð
Wearable NIR belt with infrared LEDs and camera captures stable, high-contrast vein imagery. Anti-shake elastic mount
ñ
Raspberry Pi runs advanced image preprocessing: grayscale conversion, CLAHE enhancement, top-hat filtering, vein skeletonization. System identifies longest continuous vein and selects optimal puncture point (cx, cy).
ñ
SO100ARM robotic arm executes inverse kinematics solving via
Sensing Layer
Processing Layer
Control Layer
Actuation Layer
ensurespatientcomfort during imaging.
CCD method. Motor commands transmit via Arduino and servo
drivers for perfectly aligned tip positioning.
ô
Modularend-effectors: piezoelectric puncture head for precise 2-
3mm depth control and suction head with mini vacuum pump for
consistent blood extraction.

## Slide 6
Hardware Components
6-DOF SO100ARM
Micro Vacuum Pump
NIR Imaging Module
Raspberry Pi 4B
3D-Printed Mount
Piezoelectric Actuator
Infrared camera and LEDs for vein detection across all skin tones.
Industrial-grade robotic arm engineered for medical precision and repeatability.
Gentle, consistent blood collection with pressure monitoring.
Lightweight, modular syringe attachment system for adaptability.
Real-time controller processing vision data and executing
motor commands.
Precision depth control for safe, accurate skin penetration.

## Slide 7
Software Intelligence Stack
Core Modules
Technology Foundation
Python · OpenCV · NumPy · PySerial
Image Acquisition & Enhancement: Real-time NIR preprocessing with
advanced filtering
Vein Detection: Automated identification and optimal puncture point
selection
Robotic Alignment: Inverse kinematics computation and trajectory planning
Sequence Control: Coordinated puncture initiation and suction extraction
We don't guess the vein for we compute it with mathematical precision.

## Slide 8
Integrated Workflow Demonstration
1
Align
Robot positions with precision
Capture
Wearable belt acquires vein image
Extract
Process
Puncture
Vacuum pump collects sample
Piezoactuates at exact depth
Pi analyzes and maps coordinates
End-to-end workflow: sensing through actuation, unified by real-time algorithmic control and modular hardware design.
2
3
4
5

## Slide 9
Innovation Breakthrough
Modular Architecture
Piezoelectric Precision
Simulation-Ready Design
Vision-Robotics Integration
CCD-Based Kinematics
Dual-attachment end-effectors enable seamless transitions between puncture and collection tasks.
Micro-scale depth control (2-3mm) eliminates complications from over- or under-penetration.
Computer vision directly controls robotic motion for closing the feedback loop between seeing and acting.
Fully modeled and validated before
hardware deployment for reducing clinical risk and accelerating adoption.
Cyclic Coordinate Descentinverse
kinematics delivers human-like precision motion planning.

## Slide 10
Future Clinical Expansion
Surgical Expansion
MachineLearningIntegration
Portable Wireless Platform
Depth Sensing Enhancement
Autonomous vein classification and adaptive puncture strategy
refinement through clinical datasets.
Integrated tactile sensors provide real-time feedback for safer,
more confident puncture decisions.
Battery-powered, wireless-enabled version extends access to
rural clinics and resource-limited settings.
Adaptable architecture enables deployment in ENT and
specialized surgical procedures requiring precision vascular access.